## Slide 1: EKF and Smoothing-based UAV Positioning Using UWB and IMU Fusion
Jungwon Kang1, Kunwoo Park1, Gunho Sohn1, Mozhdeh Shahbazi2, Patrick Ménard3
1York University
2University of Calgary
3Centre de géomatique du Québec
June 19 2018
39th Canadian Symposium on Remote Sensing, June 19-21, 2018

## Slide 2: Contents
1. Introduction
2. EKF vs Smoothing for UAV Positioning Using UWB & IMU
3. Experimental Results
4. Conclusion & Future Work

## Slide 3
1. Introduction

## Slide 4: UAV application in GPS-denied environment
Indoor application
Bridge, Tunnel, Chimney inspection
High-rise building inspection

## Slide 5: Difficulties of Maneuvering a Drone in GPS-denied environment

## Slide 6: Alternative Sensors for UAV Positioning
Image-based Camera: highly sensitive to the surroundings
Ranging-based UWB sensor: resistant to severe multipath
PX4FLOW optical flow
camera board
Time Domain
PulsOn 440
Skybotix VI-Sensor
Decawave TREK1000
XW
YW
ZW
W
D
XS
YS
ZS
S

## Slide 7: Ultra-Wideband-Based positioning
Robust to multipath and non-line-of-sight (NLOS) effects
cm-level ranging error
Wide range applicable
Light weight, low power consumption

## Slide 8: Related Works
UWB Sole System K. Guo 2016, B. Dewberry 2016
  Issue 1: Estimation of UWB station position
  Issue 2: Trilateration & Kalman Filter
GPS-UWB Coupled System K. Hausman 2016, J. Wang 2016
  Issue 1: Relative coordination between W and S
  Issue 2: Fusion of W-based pose and S-based one
Range-Only SLAM F. Fabresse 2015
  Issue 1: Initialization with Gaussian mixture model
  Issue 2: Range-Only Simultaneous localization and mapping
Graph Optimization Approach C. Wang, 2018
Filtering based
Smoothing based

## Slide 9: Research objective
Comparison between two algorithms
A Comparison of SLAM Algorithms with Range Only Sensors [F. Herranz, 2014]
Incremental Smoothing vs. Filtering for Sensor Fusion on an Indoor UAV [S. Lange, 2013]
Which one is the best methodology for UAV positioning?
Accuracy, Robustness, Speed…etc.

## Slide 10
2. EKF vs Smoothing for UAV Positioning Using UWB & IMU
2.1 Filtering & Smoothing
2.2 EKF & Smoothing for UAV Positioning Using UWB & IMU

## Slide 11: Filtering & Smoothing (1/2)
Filtering
  Summarizing all experience with respect to the last pose,
  using a state vector and the associated covariance matrix (→ Eliminating all past poses)
  Following the 'predict / correct' approach
*The figure is excerpted from [M. Chli, 2017].
: vehicle pose at time
: th landmark

## Slide 12: Filtering & Smoothing (2/2)
Smoothing
  Minimizing the total least-squares cost function.
  Solving for the constraints between poses and landmarks.
  Can result in a globally consistent solution.
*The figure is excerpted from [M. Chli, 2017].

## Slide 13: EKF & Smoothing for UAV Positioning Using UWB & IMU (1/2)
Filtering
  EKF
IMU data
UWB data
Time
Prediction
Correction
EKF
3D linear velocity of UAV
3D bias of accelerometers in UAV body frame
3D bias of gyroscopes in UAV body frame
3D Coordinates of the UAV
Any minimal representation of 3D rotation matrix
IMU measurements of acceleration
Angular rates measured by IMU
UWB measurement model
UAV pose state
Control input

## Slide 14: EKF & Smoothing for UAV Positioning Using UWB & IMU (2/2)
Smoothing
  Building a Factor Graph & doing inference by iSAM2
IMU data
UWB data
Time
Building a factor
Inference
Smoothing
a
Finding optimal estimate
IMU Factor
UWB Factor

## Slide 15
3. Experimental Results
3.1 Simulation Results
3.2 Experiment Preparation with Real Systems

## Slide 16: Simulation
Setup
Axes configuration
*Excerpted from [I. Sa, 2017]
Ground truth trajectory
(Simulating spiral trajectory)
UWB station
Starting point
Ending point
IMU & UWB
Simulator
EKF-based
method
Smoothing-based
method
:linear velocity
: angular velocity (in world frame)
: angular velocity,
: linear acceleration,
: UWB range,
Virtual IMU & UWB data generation and its application to each method
40Hz
100Hz

## Slide 17: Simulation Result (1/3)
Result Movie

## Slide 18: Simulation Result (2/3)
UAV Orientation & Translation
  Absolute error over time
roll(), pitch(), yaw()
Unit: rad
Time (s)
Unit: m
Time (s)
EKF
Smoothing

## Slide 19: Simulation Result (3/3)
UAV Orientation & Translation
  RMS error
 | roll (rad) | pitch (rad) | yaw (rad) | x (m) | y (m) | z (m)
EKF | 0.0478 | 0.0544 | 0.0467 | 0.0392 | 0.0407 | 0.0790
Smoothing | 0.1344 | 0.0459 | 0.0651 | 0.0352 | 0.0253 | 0.0893

## Slide 20: Experiment Preparation with Real Systems (1/5)
DJI Matrice 100 with Payload
Payload Weight [kg]
UWB Module | 0.112
Intel NUC | 0.728
Payload Battery (for NUC & UWB) | 0.542
Total | 1.382
Diagonal Wheelbase | 0.65m
Weight (with TB47D battery) | 2.355kg
Max. Takeoff Weight | 3.600kg
DJI Matrice 100
드론 시스템 사진
하드웨어 구성
소프트웨어 구성
Oshawa 전경사진
전체시스템 사진(GCS, 드론 등등)
동영상

## Slide 21: Experiment Preparation with Real Systems (2/5)
ROS Package for Data Logging Using DJI Matrice 100
  Developed using ROS Kinetic in Ubuntu 16.04
Screenshot of Rviz (ROS visualization tool)

## Slide 22: Experiment Preparation with Real Systems (3/5)
UWB
Website | http://www.timedomain.com/products/pulson-440/
Dim/Weight | 56 x 103 x 18mm, 45g
Input Voltage | 4.5 to 48V DC
Interface | Ethernet, USB, Serial, SPI, CAN
Performance | accuracy: 2.1cm, data rate: 125 Hz
Max Range | 300 m to 1100 m
Time Domain PulsOn 440

## Slide 23: Experiment Preparation with Real Systems (4/5)
Indoor Space for Experiment

## Slide 24: Experiment Preparation with Real Systems (5/5)
Ground Control Station

## Slide 25
4. Conclusion & Future Work

## Slide 26: Conclusion & Future Work
Conclusion
  Implemented EKF and smoothing based UAV localization algorithms using UWB and IMU data
  Validated through simulation. (However, it is not enough. We will need more further analysis.)
Future Work
  Further analysis on comparison of EKF and Smoothing
  Validation using real experiment data